## Slide 1: Visual localization with RLOCS and Sequential Localizer
Yuchen Yang, Jiafei Xu, Xudong Zhang, Shuang Gao, Kun Jiang, Jijunnan Li, Yandong Guo
OPPO Research Institute
All authors are with OPPO Research Institute, Shanghai, China
ICCV 2021 Workshop on
Map-Based Localization for Autonomous Driving

## Slide 2: Overall pipeline
Localization
Local feature extraction
Semantic segmentation
SfM
reconstruction
Global feature extraction
Database images
Global feature extraction
Local feature extraction
Image retrieval
Feature matching &
Semantic label check
Query image
Semantic
PNP RANSAC
RLOCS[1]
[1] Zhou Y, Fan H, Gao S, et al. Retrieval and Localization with Observation Constraints[J]. arXiv preprint arXiv:2108.08516, 2021.
Relative camera pose
Image retrieval filter
SLAM
Database extension
Loose coupling
Camera pose
Re-localize failed cases
Final pose
Mapping
Sequential
localizer

## Slide 3: RLOCS-Mapping
NN
matching
Geometric Constraint
Feature matching
Colmap SfM
reconstruction
Superpoint[2]
NetVLAD[3]
Camera Intrinsic &
Image Extrinsic
Input①
Input②
Image pairs
Database images
BiSeNet-v2[4]
(pre-trained on cityscape)
Semantic point cloud
[2] DeTone D, Malisiewicz T, Rabinovich A. Superpoint: Self-supervised interest point detection and description[C]//Proceedings of the IEEE conference on computer vision and pattern recognition workshops. 2018: 224-236.
[3] Arandjelovic R, Gronat P, Torii A, et al. NetVLAD: CNN architecture for weakly supervised place recognition[C]//Proceedings of the IEEE conference on computer vision and pattern recognition. 2016: 5297-5307.
[4] Yu C, Wang J, Peng C, et al. Bisenet: Bilateral segmentation network for real-time semantic segmentation[C]//Proceedings of the European conference on computer vision (ECCV). 2018: 325-341.

## Slide 4: RLOCS-Localization
HOW[5] image retrieval
Superpoint
K Similar database images
NN Feature matching
Semantic label check
PNP RANSAC
[5] Tolias G, Jenicek T, Chum O. Learning and aggregating deep local descriptors for instance-level recognition[C]//European Conference on Computer Vision. Springer, Cham, 2020: 460-477.
BiSeNet-v2
DBSCAN &
Merge matches
PNP RANSAC
Camera pose
Query image
K PNP candidates
Before
After
Before
After

## Slide 5: Sequential localizer
Image retrieval filter
Image retrieval
Filtering
Filtered retrieval results
Use SLAM to filter out wrong retrieval results
Last localization result
SLAM relative pose
Predict Pose
Database camera
Last localization result
SLAM relative pose

## Slide 6: Sequential localizer
Database extension
Camera pose
2D-3D Matches
Monte Carlo sampling[6]
[6] I. M. Sobol, A primer for the Monte Carlo method. CRC press, 1994.
50% matches
PNP RANSAC
Sub-pose
Compare distance
distance < TH
distance > TH
Mapping
Re-localize
One frame localization
Camera pose
Use well localized cameras to help localizing other cameras

## Slide 7: Sequential localizer
SLAM & Loose coupling
Visual localization results
Failed cases
SLAM tracking
Final pose
Results of ORB-SLAM2[7]
Combine SLAM and visual localization
[7] Raúl Mur-Artal and Juan D. Tardós. ORB-SLAM2: an Open-Source SLAM System for Monocular, Stereo and RGB-D Cameras. IEEE Transactions on Robotics, vol. 33, no. 5, pp. 1255-1262, 2017.
Closest successful frame
SLAM result
Countryside
Neighborhood
Oldtown

## Slide 8: Results
After adding sequential localizer
Countryside – RLOCS

## Slide 9: Results
Neighborhood
Oldtown

## Slide 10: Summary and outlook
Advantages:
Use simple localization pipeline and SLAM
Use SLAM to improve image retrieval and sequential localization
Limitations:
Low efficiency of the localization algorithm
Localization cannot run online
Future work:
Solve limitations
Tightly couple SLAM and visual localization
Integrate more sensors

## Slide 11: Thank you
yangyuchen@oppo.com